## Slide 1
Prerequisites
1- Understanding of Digital Electronics
2- Basic Understanding of HDL programming ( Verilog/VHDL)

## Slide 2
Tools
Tools we need :
Vivado https://www.youtube.com/watch?v=eXuHADE2Buw&ab_channel=RizwanTariq
Version: 2019.1 : its freely available. installation instructions are in this video

## Slide 3: FPGA Board
Ultra96 V2
https://www.avnet.com/wps/portal/us/products/new-product-introductions/npi/aes-ultra96-v2/

## Slide 4
Objectives
Or Gate example
Understand the Simulation workflow on Vivado
  Create or_gate project
  Quick Simulation method
  Test bench method
  Third party simulators I.e. modelsim and cadence etc.
Understand the Implementation workflow on Vivado
  Synthesis: Synthesis is the process of transforming an RTL-specified design into a gate-level representatio
  Synthesize with out constraints.
  Adding Constraints
    How to read constraints from FPGA board User guide
    Adding constraints using GUI
    Adding constraints using XDC file
  Implementation
    Vivado implementation includes all steps necessary to place and route the netlist onto the FPGA device resources, while meeting the logical, physical, and timing constraints of a design.
  Generate Bitstream
  Connect FPGA board to PC/Laptop
    if the FPGA board is not detected by Vivado, check device manager if the drivers are installed. If not, please install drivers.
  Program the FPGA

## Slide 5: Objectives
Use ILA: Second Method
  Monitoring of internal signals i.e. states of state machine
ILA + VIO = very powerful debugging of FPGA designs

## Slide 6: Objectives
Use Vivado Block Design
Use Virtual I/O to interact with the design
  Virtual Input/Output (VIO) core is a customizable core that can both monitor and drive internal FPGA signals in real time.
  VIO requires clock
    In Ultra96, I have to get clock from Zynq Processing System
    This requires a bit understanding of HW/SW codesign.
    I have explained HW/SW co-design concepts in these two vides in detail
    https://www.youtube.com/watch?v=xb7QBuBZuvI&ab_channel=RizwanTariq
    https://www.youtube.com/watch?v=bs3bzgAZqqw&t=1s&ab_channel=RizwanTariq

## Slide 7: Vivado Block Design
My Block Design: Zynq PS provides Clock
Alternative Approach: Provide External Clock directly
Alternative Approach: Provide External Clock via Clocking Wizard

## Slide 8: Objectives
Use ILA
  Integrated Logic Analyzer (ILA) IP core is a logic analyzer core that can be used to monitor the internal signals of a design
  Save the data for post processing
  Different Trigger combinations
ILA + VIO = very powerful debugging of FPGA designs
Example:
  Data Capture from a sensor. If the sensor is a Radar. Then we can capture the radar data on a Trigger, save that data in a excel file, and can use that for post processing (e.g. FFT) ( MATLAB, OCTAVE, Python etc. )

## Slide 9: Vivado Block Design
My Block Design: Zynq PS provides Clock